## Slide 1: Save a Bit, Shift a Bit, blink a 100 LEDs!
Hollo-deck presentation for the Lab Work
Presented by charmstr

## Slide 2: What we are going to see:
An Introduction to Logic gates
What is memory ? how to save a bit
What is a register ? A shift register?
A insight into the basics of Computer architecture
SIPO: Serial in Parallel out
How to Control a lot of LEDs with only 3 control pins

## Slide 3: LOGIC GATES
They are the basic of electronic logic circuitry.
AND, OR, NOT, XOR
They do the same logic job as their equivalent in C language…
Example:
  if ( a && b )
a == 1 ?
b == 1 ?
0 or 1
AND

## Slide 4
Logic 1?
  “HIGH” = near +5V
Logic 0?
  “LOW” or near 0V…
In between? What is 2,5V?
  /!\ We don’t know /!\ We will see later the “tri-state output”
a == 1 ?
b == 1 ?
0 or 1
We are in +5V today…
AND

## Slide 5: LOGIC GATES SYMBOLS
NOT gate (inverter):
AND gate:
NAND gate:
OR gate:
NOR gate:

## Slide 6: What is memory ? how to save a bit

## Slide 7: NOR latch introduction
video from Ben eater’s YouTube channel (play between 02:00 and 03:42):
https://www.youtube.com/watch?v=KM0DdEaY5sY

## Slide 8: REMEMBER?
The astable multi-vibrator

## Slide 9: Bi-stable multi-vibrator
It has two absolutely stable states
It is also called a flip-flop, trigger circuit or binary

## Slide 10
Latched/stable state
HIGH
OUTPUT ?
0V (Ground)
+5V
+5V
0V
Ground

## Slide 11
SET
RESET
We can set and Reset: Bi-stable

## Slide 12: Lets forget about transistors… and just use logic circuits
We will use components from the 74 series.(ex: SN7400, 74LVxx…)
Originally started by Texas Instrument and then adopted as a standard among other manufacturers.
This is old school.

## Slide 13
Therefore inverted Q is LOW
Imagine Q is HIGH at the very start
Lets say we start in this situation
0V
0V
inversion
NOR = OR + NOT
inversion
If Reset does not change to go HIGH…
The OUTPUT Q will stay HIGH forever*
If Set is toggled, it does not change anything
1 OR 1 …
1 OR 0 …
INPUTS
OUTPUTS
Q is going to be the bit we save in memory: 0 OR 1
Lets forget about inverted Q

## Slide 14: Today you will build a LATCH with NAND gates
Equivalent circuit
/!\ be careful: Not + OR NOR
We will use it in the next slides…

## Slide 15: a bit in memory OK, we need a clock signal
We just need to add AND gates!
But NAND gates are cheaper.
Our latch
Two inversions in a raw cancel each other in Boolean Logic.
But realistically there is still a delay… (in nano seconds, see documentation)

## Slide 17
AND
OR

## Slide 18: The D latch
Since the RS flip flop is susceptible to a race condition …

## Slide 19: Clocked D latch
Nothing really new.
Now we have just one input in our diagram.

## Slide 20: The need for Edge-triggered lacthing
One clock cycle, and several changes in the Q Output  We don’t want that.

## Slide 21: Edge triggering
Components Can be positive edge-triggered
or Negative edge-triggered
An example of positive edge-triggering with a RC
RC time constant much smaller than the clock cycle in the design

## Slide 22: Edge triggering
In processors this won’t be done with RC circuits
Capacitors are too big, too difficult to fabricate on a chip…
Now the output can change only on the rising (or falling) edge of the clock
   We sample the incoming data bit only at one instant during the clock cycle

## Slide 23: Preset and Reset/Clear

## Slide 24: Preset at start up time
+VCC
+VCC
P
P

## Slide 26: Registers
We know how to save one bit in our Latch, and its edge-triggered with the clock signal(raising or falling)
PRESET
CLEAR

## Slide 27: What is a register?
4 Bits

## Slide 28: What is a Shift Register?
Common Clock
Q Output goes into the next Data IN

## Slide 29: We can add control lines to our register
Ex: Load Data (usually “Latch enable” or “Store enable”)
Same logic for “OUTPUT ENABLE”, “PRESET”, ”CLEAR”…

## Slide 30: Controlled Shift register
OR

## Slide 31: SIPO: Serial In Parallel Out
PISO exists as well: Parallel In Serial out
  Example: before sending information via UART protocol, it is stored into a buffer register in parallel at some point, then shifted out in serial
DATA IN
DATA OUT
CLOCK

## Slide 32: How may LEDs can you control?

## Slide 33: Binary - 0 or 1 - WTF is the tri-state output?
+VCC
ENABLE
DATA IN
DATA OUT

## Slide 34: Computer architecture insight
MEMORY A
MEMORY B
MEMORY C
MEMORY
DATA BUS
ADDRESS BUS
INPUT
INPUT
INPUT
INPUT
OUTPUT
OUTPUT
OUTPUT
OUTPUT
Selected line
CLK
A
D
A
Selected line
A

## Slide 35: Sources

## Slide 36: Lab Work / TP : components

## Slide 37: TP todo list
https://github.com/charMstr/Save_a_bit_Shift_bits_Blink_100_ledss.git

## Slide 38: Pendant ce temps là

## Slide 39
charmstr